## Slide 1: ISO 15118: The Next Generation of EV Charging Communication
Comparing ISO 15118 with OCPP 1.6: Benefits for Vendors, Grid, and Users

## Slide 2: Agenda
• Introduction to EV Charging Protocols
• OCPP 1.6 Overview & Architecture
• ISO 15118 Overview & Architecture
• System Architecture Comparison
• Workflow Diagrams
• Key Differences Comparison
• Advantages for Different Stakeholders
• Implementation Challenges
• Future Outlook
• References & Resources

## Slide 3: Introduction to EV Charging Protocols
Why Communication Protocols Matter:
  • Interoperability: Seamless charging across different networks
  • Security: Secure data exchange between EV and charging station
  • User Experience: Plug-and-charge convenience
  • Grid Integration: Smart charging and demand response
  • Billing: Automated payment processing
Evolution Timeline:
  • 2012: OCPP 1.5 released
  • 2015: OCPP 1.6 released
  • 2015: ISO 15118-2 published
  • 2022: ISO 15118-20 (V2G) published

## Slide 4: OCPP 1.6 Overview
What is OCPP 1.6?
  • Open Charge Point Protocol 1.6
  • WebSocket-based communication
  • JSON message format
  • Central System to Charge Point communication
Key Features:
  ✅ Real-time communication
  ✅ Transaction management
  ✅ Remote configuration
  ✅ Firmware updates
  ✅ Security (TLS encryption)
  ✅ Extensible message structure
Limitations:
  ❌ No direct EV-to-charging station communication
  ❌ Manual authentication required
  ❌ Limited smart charging capabilities
  ❌ No vehicle-to-grid (V2G) support

## Slide 5: OCPP 1.6 System Architecture
OCPP 1.6 Communication Flow:
┌─────────────────┐ WebSocket ┌──────────────────┐ HTTP/REST ┌─────────────────┐ │ Electric │ ◄──────────────► │ Charging │ ◄──────────────► │ Central │ │ Vehicle │ │ Station │ │ System │ │ │ │ │ │ │ │ • No direct │ │ • OCPP Client │ │ • Backend │ │ communication │ │ • WebSocket │ │ Services │ │ • Manual auth │ │ Connection │ │ • Database │ │ • RFID/App │ │ • JSON Messages │ │ • Billing │ └─────────────────┘ └──────────────────┘ └─────────────────┘
Key Components:
  • Charging Station: OCPP client with WebSocket connection
  • Central System: Backend server managing multiple stations
  • Communication: JSON messages over WebSocket protocol
  • Authentication: Manual via RFID, mobile app, or manual input

## Slide 6: OCPP 1.6 Charging Workflow
OCPP 1.6 Charging Process:
1. User arrives at charging station 2. Manual authentication required: ├─ RFID card swipe ├─ Mobile app scan └─ Manual input (PIN/card) 3. Station sends authentication to Central System 4. Central System validates and authorizes 5. Station starts charging session 6. Real-time status updates via WebSocket 7. Charging session monitoring 8. Session termination 9. Billing and payment processing 10. Receipt generation

## Slide 7: ISO 15118 Overview
What is ISO 15118?
  • International standard for EV charging communication
  • Direct communication between EV and charging station
  • PLC (Power Line Communication) or wireless
  • Plug-and-Charge (PnC) capability
Key Components:
  • ISO 15118-1: General information and use-case definition
  • ISO 15118-2: Network and application protocol requirements
  • ISO 15118-3: Physical and data link layer requirements
  • ISO 15118-4: Network and application protocol conformance testing
  • ISO 15118-5: Physical layer and data link layer conformance testing
  • ISO 15118-8: Physical layer and data link layer requirements for wireless communication
  • ISO 15118-20: 2nd generation network and application protocol requirements

## Slide 8: ISO 15118 System Architecture
ISO 15118 Communication Flow:
┌─────────────────┐ ISO 15118 ┌──────────────────┐ OCPP/HTTP ┌─────────────────┐ │ Electric │ ◄──────────────► │ Charging │ ◄──────────────► │ Central │ │ Vehicle │ │ Station │ │ System │ │ │ │ │ │ │ │ • ISO 15118 │ │ • ISO 15118 │ │ • Backend │ │ Client │ │ Server │ │ Services │ │ • Digital │ │ • PLC/Wireless │ │ • PKI │ │ Certificate │ │ • OCPP Client │ │ • V2G Services │ └─────────────────┘ └──────────────────┘ └─────────────────┘
Key Components:
  • Electric Vehicle: ISO 15118 client with digital certificate
  • Charging Station: ISO 15118 server + OCPP client
  • Communication: ISO 15118 over PLC/Wireless + OCPP over WebSocket
  • Authentication: Automatic via PKI digital certificates

## Slide 9: ISO 15118 Plug-and-Charge Workflow
ISO 15118 Plug-and-Charge Process:
1. User plugs in EV to charging station 2. Automatic ISO 15118 handshake: ├─ Vehicle identification ├─ Digital certificate exchange └─ Authentication validation 3. Station requests charging parameters from vehicle 4. Vehicle provides: ├─ Battery capacity and state ├─ Charging preferences └─ Payment information 5. Station starts charging session 6. Real-time communication during charging 7. V2G capabilities (if supported) 8. Session termination 9. Automatic billing and payment 10. Receipt sent to vehicle/user

## Slide 10: System Architecture Comparison
OCPP 1.6 vs ISO 15118 Architecture:
OCPP 1.6 Architecture: ┌─────────┐ WebSocket ┌─────────┐ HTTP/REST ┌─────────┐ │ EV │ ◄──────────────► │ Station │ ◄──────────────► │ Central │ │ (No Dir)│ │ │ │ System │ └─────────┘ └─────────┘ └─────────┘ ISO 15118 Architecture: ┌─────────┐ ISO 15118 ┌─────────┐ OCPP/HTTP ┌─────────┐ │ EV │ ◄──────────────► │ Station │ ◄──────────────► │ Central │ │ (Direct)│ │ │ │ System │ └─────────┘ └─────────┘ └─────────┘
Key Architectural Differences:
  • OCPP 1.6: No direct EV communication
  • ISO 15118: Direct EV-to-station communication
  • OCPP 1.6: Manual authentication required
  • ISO 15118: Automatic authentication via PKI
  • OCPP 1.6: Limited vehicle data
  • ISO 15118: Rich vehicle information exchange

## Slide 11: Workflow Comparison
OCPP 1.6 vs ISO 15118 Workflow:
OCPP 1.6 Workflow: 1. User arrives → 2. Manual auth → 3. Station auth → 4. Start charging 5. Monitor → 6. Stop → 7. Manual billing → 8. Receipt ISO 15118 Workflow: 1. Plug in → 2. Auto handshake → 3. Get params → 4. Start charging 5. Monitor → 6. Stop → 7. Auto billing → 8. Auto receipt
Workflow Differences:
  • Authentication: Manual vs Automatic
  • User Experience: Multiple steps vs Plug-and-Charge
  • Data Exchange: Limited vs Rich vehicle information
  • Billing: Manual processing vs Automatic
  • V2G Support: Not available vs Full support

## Slide 12: Key Differences: Communication Architecture
OCPP 1.6 Architecture:
[EV] ←→ [Charging Station] ←→ [Central System] ←→ [Backend Services]
ISO 15118 Architecture:
[EV] ←→ [Charging Station] ←→ [Central System] ←→ [Backend Services]
(Direct Communication)
Key Differences:
  • Communication Path: Central System ↔ Charging Station vs EV ↔ Charging Station
  • Authentication: Manual (RFID, App) vs Automatic (Digital Certificate)
  • Data Exchange: Limited vehicle data vs Rich vehicle information
  • Security: TLS encryption vs PKI-based security

## Slide 13: Advantages for Vendors
Hardware Vendors:
  ✅ Higher-value charging stations
  ✅ Advanced features and capabilities
  ✅ Competitive differentiation
  ✅ Future-proof technology
Software Vendors:
  ✅ Rich data for analytics
  ✅ Advanced billing systems
  ✅ Grid integration services
  ✅ V2G platform opportunities
Service Providers:
  ✅ Enhanced user experience
  ✅ Automated operations
  ✅ Reduced manual intervention
  ✅ New revenue streams

## Slide 14: Advantages for Grid Operators
Smart Grid Integration:
  ✅ Demand response capabilities
  ✅ Load balancing
  ✅ Grid stability
  ✅ Renewable energy integration
Vehicle-to-Grid (V2G) Benefits:
  ✅ Bidirectional power flow
  ✅ Grid stabilization
  ✅ Peak shaving
  ✅ Frequency regulation
Data & Analytics:
  ✅ Real-time load monitoring
  ✅ Predictive analytics
  ✅ Grid planning insights
  ✅ Efficiency optimization

## Slide 15: Advantages for Users
Enhanced User Experience:
  ✅ Plug-and-Charge convenience
  ✅ No manual authentication needed
  ✅ Automatic billing
  ✅ Seamless roaming
Cost Benefits:
  ✅ Optimized charging costs
  ✅ Time-of-use pricing
  ✅ V2G revenue opportunities
  ✅ Reduced transaction fees
Environmental Benefits:
  ✅ Smart charging for renewables
  ✅ Grid decarbonization support
  ✅ Reduced carbon footprint
  ✅ Sustainable energy integration

## Slide 16: Implementation Challenges
Technical Challenges:
  🔧 Complex PKI infrastructure
  🔧 Hardware compatibility
  🔧 Software integration
  🔧 Testing and certification
Business Challenges:
  🔧 High implementation costs
  🔧 Limited vendor support
  🔧 Market adoption time
  🔧 ROI uncertainty
Regulatory Challenges:
  🔧 Standards compliance
  🔧 Regional variations
  🔧 Certification requirements
  🔧 Interoperability testing

## Slide 17: Future Outlook
Market Trends:
  📈 Growing EV adoption
  📈 Smart grid development
  📈 V2G market expansion
  📈 Renewable energy integration
Technology Evolution:
  📈 ISO 15118-20 adoption
  📈 Wireless communication
  📈 Advanced V2G capabilities
  📈 AI integration
Timeline Projection:
  📈 2024-2025: Early adoption phase
  📈 2026-2028: Mass market adoption
  📈 2029-2030: Full market penetration

## Slide 18: Conclusion
Key Takeaways:
  🎯 ISO 15118 is the future of EV charging
  🎯 Significant advantages over OCPP 1.6
  🎯 Benefits all stakeholders
  🎯 Investment in future technology
Next Steps:
  ➡️ Assess current infrastructure
  ➡️ Plan migration strategy
  ➡️ Engage with vendors
  ➡️ Monitor market developments

## Slide 19: References & Resources
Official Standards:
  • ISO 15118-1:2019: General information and use-case definition
  • ISO 15118-2:2016: Network and application protocol requirements
  • ISO 15118-3:2016: Physical and data link layer requirements
  • ISO 15118-20:2022: 2nd generation network and application protocol requirements
Industry Organizations:
  • CharIN e.V.: Charging Interface Initiative
  • OCA: Open Charge Alliance
  • IEC: International Electrotechnical Commission
  • SAE International: Society of Automotive Engineers

## Slide 20: Thank You!
Questions & Discussion
Contact Information:
📧 Email: [Your Email]
📱 Phone: [Your Phone]
🌐 Website: [Your Website]